## Slide 1: Bypassing Palo Alto Firewall Rules One Packet at a Time
Dave Lassalle
NolaSec Presentation
9/27/2012

## Slide 2: About Me
Involved with InfoSec for 9 years
DM Petroleum Operations
  M&O Contractor for Strategic Petroleum Reserve
Senior Cyber Security Engineer
  Security Monitoring, Incident Detection, Incident Response
  Risk Analyses and Compliance Paperwork
  Maintain and Administer Security tools
    Including Firewalls…

## Slide 3: Egress Buster
Released in February by Dave Kennedy (@dave_rel1k)
Useful for finding what ports are open from within a network to the Internet
Helpful with determining reverse shell port
Run server on a range of ports and tell the client to try to connect on every port

## Slide 4: Egress Buster Expected Results
Server
Client

## Slide 5: Logs during Blocked Egress Buster run
All traffic to the server in that port range is denied.

## Slide 6: Egress Buster Actual Results
Well, there’s supposed to be a firewall there. What’s going on?
Server
Client

## Slide 7: Firewall Overview
Traditional Firewall
Next-Gen Firewall
Application Layer
Added features
  “IPS” features
    AV
    Vulnerability Detection
    DLP
  Application Identification
Network and Transport Layer
Allow/Deny rules based on:
  Source IP, Port
  Destination IP, Port

## Slide 8: Rules Used in Test
Allow web browsing, ssl, and skype on their default ports.

## Slide 9: Application Definitions
“ssl” application

## Slide 10: Application Definitions
“web-browsing” application

## Slide 11: Application Definitions
“skype” application

## Slide 12: Why Egress Buster is allowed
App-ID requires some traffic be allowed
  TCP handshake and at least 1 packet of payload
Skype’s port tcp/dynamic
  At least 1 packet allowed on ALL PORTS
Connection will be dropped if payload is not actual Skype traffic
At least 1 packet of data has already egressed

## Slide 13: Logs during Egress Buster run
Top: Expected logs when traffic is blocked (as shown on earlier slide)
Bottom: Actual logs when traffic is allowed. Application is insufficient-data because it’s still trying to identify.

## Slide 14: How Many Packets Get Through?
Tested with netcat
Typing a few characters on command line
  10-12 packets allowed
  ~40-50 bytes allowed
Piping a file into netcat
  2-4 full 1460 byte packets allowed
  2920-5840 bytes allowed
All you need is one

## Slide 15: Logs during netcat test showing kills eventually
Traffic is allowed and type is incomplete
3 of 4 made it
9 of 10 made it
Client
Server

## Slide 16: Palo Alto Response
Working as expected
Not a proxy
Inspecting the packet before releasing would impact performance
Traditional firewall would let all packets through, not just first
  Fair enough

## Slide 17: Taking Advantage of the Rules
At least 1 packet will always be allowed
Need something to send data with 1 packet per TCP session
  TCP handshake
  Send 1 full packet
  Close session
  Repeat until input is done

## Slide 18: ngfw_egress.pl
First attempt
Few different modes
  Will show an example of the file transfer mode

## Slide 19: ngfw_egress.pl server and client commands
Server: ./ngfw_egress.pl –w Putty.exe –l –p 80
Client: perl ngfw_egress.pl –r Putty.exe egresstest 80
Server
Client
1
2
3
4
6
7
5

## Slide 20: Logs during ngfw_egress.pl run
Traffic is allowed and type is insufficient-data
9 Packets:
Handshake (3): SYN, SYN/ACK, ACK
Data Transfer (2): PSH/ACK, ACK
Teardown (4): FIN, ACK, FIN, ACK

## Slide 21: Defenses
Limit destination IP address, if possible
Limit ports, if possible
Use a Proxy with Protocol Detection
Very noisy
  Monitor logs
  High # of connections, little data per connection

## Slide 22: Future Plans
Perl Script already has more features
  Delay, MSS (potential IDS/DLP evasion), interactive mode
  Problems with attaching to shell
Trying a bash script that calls netcat
  Wouldn’t require Perl installed
  Can use netcat’s “-e” option directly
  Not sure how painful cmd.exe version will be
Metasploit handler and payload
Would love to know if it works with others
  Fortinet, SonicWall, etc.

## Slide 23: Code and Updates
Code on GitHub:
  https://github.com/superponible
Updates and Information:
  http://superponible.com
  @superponible

## Slide 24: Questions/Comments?
Contact:
  dave@superponible.com
  @superponible
  http://superponible.com